The exponential growth of computing power and personal computer ownership made the

computer one of the most important forces that shaped business and society in the second half

of the twentieth century. Computers are expected to continue to play crucial roles in the growth

of technology, business, and new arenas.

The IA-32 Intel Architecture has been at the forefront of the computer revolution and is today

the preferred computer architecture, as measured by the computers in use and total computing

power available in the world. The two major factors that drive the popularity of IA-32 architec-

ture are: (1) software compatibility (2) and the fact that each generation of IA-32 processors

delivers significantly higher performance.

This chapter provides a brief historical summary of the IA-32 architecture, from the Intel 8086

processor to the latest version implemented in the Pentium 4 and Intel Xeon processors.

2.1.

BRIEF HISTORY OF THE IA-32 ARCHITECTURE

One of the most important achievements of the IA-32 architecture is that object code created for

processors released in 1978 still executes on the latest processors in the IA-32 architecture

family.

2.1.1.

The First Microprocessors

The IA-32 architecture can be traced to Intel 8085 and 8080 microprocessors and to the Intel

4004 microprocessor (the first microprocessor, designed by Intel in 1969). The IA-32 architec-

ture family was preceded by 16-bit processors which include the 8086 and the 8088 processors.

The 8086 has 16-bit registers and a 16-bit external data bus, with 20-bit addressing giving a

1-MByte address space. The 8088 is similar to the 8086 except it has an 8-bit external data bus.

These processors introduced segmentation to the IA-32 architecture. With segmentation, a 16-

bit segment register contains a pointer to a memory segment of up to 64 KBytes. Using four

segment registers at a time, the 8086/8088 processors are able to address up to 256 KBytes

without switching between segments. The 20-bit addresses that can be formed using a segment

register and an additional 16-bit pointer provide a total address range of 1 MByte.

2-1

Intel Architecture

INTRODUCTION TO THE IA-32 INTEL ARCHITECTURE

2.1.2.

Introduction of Protected Mode Operation

The Intel 286 processor introduced protected mode operation into the IA-32 architecture.

Protected mode uses the segment register contents as selectors or pointers into descriptor tables.

Descriptors provide 24-bit base addresses, maximum physical memory size of up to 16 MBytes,

support for virtual memory management on a segment swapping basis, and various protection

mechanisms. The protection mechanisms include: segment limit checking, read-only and

execute-only segment options, and up to four privilege levels to protect operating system code

(in several subdivisions, if desired) from application or user programs. In addition, hardware

task switching and local descriptor tables allow the operating system to protect application or

user programs from each other.

2.1.3.

Advent of 32-bit Processors

The Intel386 processor was the first 32-bit processor in the IA-32 architecture family. In 1985,

it introduced 32-bit registers for use both to hold operands and for addressing. The lower half of

each 32-bit Intel386 register retains the properties of the 16-bit registers of earlier generations.

This permits complete backward compatibility. The processor also provides a virtual-8086

mode that allows for greater efficiency when executing programs created for the 8086 and 8088

processors.

The Intel386 processor has a 32-bit address bus and supports up to 4 GBytes of physical

memory. Logical address space is provided for each software process. The 32-bit architecture

supports both a segmented-memory model and a flat1 memory model. In the flat memory model,

segment registers point to the same address. All 4 GBytes of addressable space within each

segment are accessible.

Earlier 16-bit instructions were enhanced with new Intel386 32-bit operands and addressing

forms. The processor also introduced paging, with the fixed 4 KByte page size providing a

method for virtual memory management that is superior to using segments for this purpose.

Intel386 processor was the first to include a number of parallel stages. The six stages are: the

bus interface unit (accesses memory and I/O for the other units), the code prefetch unit (receives

object code from the bus unit and puts it into a 16-byte queue), the instruction decode unit

(decodes object code from the prefetch unit into microcode), the execution unit (executes the

microcode instructions), the segment unit (translates logical addresses to linear addresses and

does protection checks), and the paging unit (translates linear addresses to physical addresses,

does page based protection checks, and contains a cache with information for up to 32 most

recently accessed pages).

2.1.4.

The Intel486™ Processor

The Intel486™ processor, introduced in 1989, added additional parallel execution capability by

expanding the Intel386 processor’s instruction decode and execution units into five pipelined

stages. Each each stage operates in parallel with the others on up to five instructions in different

1. Requires only one 32-bit address component to access anywhere in the linear address space.

2-2

INTRODUCTION TO THE IA-32 INTEL ARCHITECTURE

stages of execution. Each stage can do its work on one instruction in one clock, so the Intel486

processor can execute as rapidly as one instruction per clock cycle.

An 8-KByte on-chip first-level cache was added to the Intel486 processor to greatly increase the

percent of instructions that could execute at the scalar rate of one per clock. Memory access

instructions are included if the operand is in the first-level cache.

The Intel486 processor also added an integrated x87 FPU.

Subsequent generations of the Intel486 processor incorporated new power saving and system

management capabilities. These features were initially developed for processors targeted at the

notebook PC market (the Intel386 SL and Intel486 SL processors). They include: System

Management Mode (triggered by a dedicated interrupt pin), the Stop Clock, and Auto Halt

Powerdown.

2.1.5.

The Intel® Pentium® Processor

The introduction of the Intel Pentium processor in 1993 added a second execution pipeline to

achieve superscalar performance (two pipelines, known as u and v, together can execute two

instructions per clock). The on-chip first-level cache doubled, with 8 KBytes devoted to code and

another 8 KBytes devoted to data. The data cache uses the MESI protocol to support the more

efficient write-back cache in addition to the write-through cache previously used by the Intel486

processor. Branch prediction with an on-chip branch table was added to increase performance

in looping constructs.

Extensions were added to make the virtual-8086 mode more efficient and to allow for 4-MByte

as well as 4-KByte pages. The processor registers are still 32 bits, but internal data paths of 128

and 256 bits add speed to internal data transfers. The burstable external data bus was increased

to 64 bits. An Advanced Programmable Interrupt Controller (APIC) was added to support

systems with multiple Pentium processors. New pins and a special mode (dual processing) were

designed in to support glueless two processor systems.

A subsequent stepping of the Pentium family introduced Intel MMX Technology (the Pentium

Processor with MMX technology). Intel MMX technology uses the single-instruction, multiple-

data (SIMD) execution model to perform parallel computations on packed integer data

contained in 64-bit MMX registers. This technology greatly enhanced the performance in

advanced media, image processing, and data compression applications.

2.1.6.

The P6 Family of Processors

Intel introduced the P6 family of processors in 1995. This processor family was based on a

superscalar micro-architecture that set new performance standards. One of the goals in the

design of the P6 family micro-architecture was to exceed the performance of the Pentium

processor significantly while using the same 0.6-micrometer, four-layer, metal BICMOS manu-

facturing process. This meant that performance gains could only be achieved through substantial

advances in the micro-architecture.

2-3

INTRODUCTION TO THE IA-32 INTEL ARCHITECTURE

The Intel Pentium Pro processor was the first processor based on the P6 micro-architecture.

Subsequent members of the P6 processor family include: the Intel Pentium II, Intel Pentium®

II Xeon™, Intel Celeron®, Intel Pentium III, and Intel Pentium® III Xeon™ processors.

The Pentium Pro processor is three-way superscalar. By using parallel processing techniques,

the processor is able on average to decode, dispatch, and complete execution of (retire) three

instructions per clock cycle. The processor also introduced the dynamic execution (the micro-

data flow analysis, out-of-order execution, superior branch prediction, and speculative execu-

tion) in a superscalar implementation. Three instruction decode units work in parallel to decode

object code into smaller operations called micro-ops (micro-architecture op-codes). These

micro-ops are fed into an instruction pool and (when interdependencies permit) can be executed

out of order by the five parallel execution units (two integer, two FPU and one memory interface

unit). The Retirement Unit retires completed micro-ops in their original program order, taking

branches into account.

The Pentium Pro processor was further enhanced by its caches. It has the same two on-chip

8 KByte 1st-Level caches as the Pentium processor and an additional 256 KByte 2nd-Level

cache in the same package as the processor. The 256 KByte 2nd-Level cache uses a dedicated

64-bit backside (cache-bus) full clock speed bus. The 1st-Level cache is dual-ported, the 2nd-

Level cache supports up to 4 concurrent accesses. The 64-bit external data bus is transaction-

oriented, meaning that each access is handled as a separate request and response with numerous

requests allowed while awaiting a response.

The Pentium Pro processor’s expanded 36-bit address bus gives a maximum physical address

space of 64 GBytes.

The Intel Pentium II processor added Intel MMX Technology to the P6 family processors along

with new packaging and several hardware enhancements. The processor core is packaged in the

single edge contact cartridge (SECC), enabling ease of design and flexible motherboard archi-

tecture. The 1st-Level data and instruction caches were enlarged to 16 KBytes each, and 2nd-

Level cache sizes of 256 KBytes, 512 KBytes, and 1 MByte are supported. A half-clock speed

backside bus connects the 2nd-Level cache to the processor. Multiple low-power states such as

AutoHALT, Stop-Grant, Sleep, and Deep Sleep are supported to conserve power when idling.

The Pentium II Xeon processor combined premium characteristics of previous generations of

Intel processors. This includes: 4-way, 8-way (and up) scalability and a 2 MByte 2nd-Level

cache running on a full-clock speed backside bus.

The Intel Celeron processor family focused the IA-32 architecture on the desktop or value PC

market segment. It offers an integrated 128 KByte of Level 2 cache and a plastic pin grid array

(P.P.G.A.) form factor to lower system design cost.

The Pentium III processor introduced the Streaming SIMD Extensions (SSE) to the IA-32 archi-

tecture. SSE extensions expand the SIMD execution model introduced with the Intel MMX

technology by providing a new set of 128-bit registers and the ability to perform SIMD opera-

tions on packed single-precision floating-point values.

The Pentium III Xeon processor extended the performance levels of the IA-32 processors with

the enhancement of a full-speed, on-die, and Advanced Transfer Cache.

2-4

INTRODUCTION TO THE IA-32 INTEL ARCHITECTURE

2.1.7.

The Intel Pentium 4 Processor

In 2000, the Intel Pentium 4 processor introduced the Intel NetBurst micro-architecture. The

Intel NetBurst micro-architecture allows processors to operate at significantly higher clock

speeds and performance levels than previous IA-32 processors.

The processor has the following features:

•

Intel NetBurst micro-architecture (see Section 2.2.3., The Intel® NetBurst™ Micro-Archi-

tecture for a detailed description)

— Rapid Execution Engine

— Hyper Pipelined Technology

— Advanced Dynamic Execution

— Innovative cache subsystem2

•

Streaming SIMD Extensions 2 (SSE2)

— Extends the Intel MMX Technology and the SSE extensions with 144 new instruc-

tions; these include support for:

•

•

•

128-bit SIMD integer arithmetic operations

128-bit SIMD double precision floating point operations

Cache and memory management operations

— Enhances and accelerates video, speech, encryption, image and photo processing

•

A 400 MHz Intel NetBurst micro-architecture system bus; this includes:

— 3.2 GBytes per second throughput (3 times faster than the Pentium III processor)

— Quad-pumped 100 MHz scalable bus clock achieves 400 MHz effective speed

— Split-transaction, pipelined

— 64-byte line size with 128-byte accesses

— Support for higher data throughput with higher bus clock

•

•

Support for Hyper-Threading Technology (see Section 2.2.4., Hyper-Threading

Technology)

Compatible with applications and operating systems written to run on Intel IA-32 archi-

tecture processors

2. The Intel Pentium 4 processor uses a cache line size of 64 bytes throughout its cache hierarchy. The

larger unified cache levels use a sectored implementation, where each 128-byte cache sector consists of

two associated 64-byte cache lines.

2-5

INTRODUCTION TO THE IA-32 INTEL ARCHITECTURE

2.1.8.

The Intel® Xeon™ Processor

The Intel Xeon processor is based on the Intel NetBurst micro-architecture (see Section 2.2.3.,

The Intel® NetBurst™ Micro-Architecture). This family of IA-32 processors is designed for use

in server systems and high-performance workstations. The Intel Xeon processor has the same

advanced features as the Pentium 4 processor (see Section 2.1.7., The Intel Pentium 4

Processor).

2.1.9.

The Intel® Pentium® M Processor

The Intel Pentium M processor is a high performance, low power mobile processor with micro-

architectural enhancements over previous generations of Intel mobile processors. The Pentium

M processor includes the following features:

•

•

•

•

•

•

•

•

Supports Intel Architecture with Dynamic Execution

High performance, low-power core

On-die, primary 32-kbyte instruction cache and 32-kbyte write-back data cache

On-die, 1-MByte second level cache with Advanced Transfer Cache Architecture

Advanced Branch Prediction and Data Prefetch Logic

Streaming SIMD Extensions 2 (SSE2)

400 MHz, Source-Synchronous Processor System Bus

Advanced Power Management features including Enhanced Intel® SpeedStep® Technology

The Intel Pentium M processor is manufactured using Intel’s advanced 0.13 micron process

technology with copper interconnect. The processor supports MMX™ Technology, Streaming

SIMD instructions, and the SSE2 instruction set. It is fully compatibility with IA-32 software.

The high performance core features innovations like Micro-op Fusion and Advanced Stack

Management. These reduce the number of µops handled by the processor and this results in

more efficient scheduling and better performance at low power. On-die 32-KB first-level

instruction and data caches and a 1 MByte second-level cache with Advanced Transfer Cache

Architecture deliver significant performance improvements over previous generations of mobile

Intel processors.

The processor also features advanced branch prediction architecture that significantly reduces

the number of mispredicted branches. The processor’s Data Prefetch Logic speculatively fetches

data to the second-level cache before a cache request to the first-level data cache occurs. This

results in reduced bus cycle penalties.

2.2.

MORE ON MAJOR TECHNICAL ADVANCES

The following sections provide more information on major additions to the IA-32 architecture.

2-6

INTRODUCTION TO THE IA-32 INTEL ARCHITECTURE

2.2.1.

The P6 Family Micro-architecture

The Pentium Pro processor introduced a new micro-architecture for the Intel IA-32 processors,

commonly referred to as P6 processor microarchitecture. The P6 processor micro-architecture

was later enhanced with an on-die, 2nd-Level cache, called Advanced Transfer Cache.

This micro-architecture is a three-way superscalar, pipelined architecture. Three-way super-

scalar means that using parallel processing techniques, the processor is able on average to

decode, dispatch, and complete execution of (retire) three instructions per clock cycle.

To handle this level of instruction throughput, the P6 processor family uses a decoupled, 12-

stage superpipeline that supports out-of-order instruction execution. Figure 2-1 shows a concep-

tual view of the P6 processor micro-architecture pipeline with the Advanced Transfer Cache

enhancement.

System Bus

Frequently used

Bus Unit

Less frequently used

2nd Level Cache

On-die, 8-way

1st Level Cache

4-way, low latency

Front End

Execution

Instruction

Cache

Microcode

ROM

Fetch/

Decode

Execution

Out-of-Order Core

Retirement

Branch History Update

BTSs/Branch Prediction

Figure 2-1. The P6 Processor Micro-Architecture with Advanced Transfer

Cache Enhancement

To insure a steady supply of instructions and data for the instruction execution pipeline, the P6

processor micro-architecture incorporates two cache levels. The Level 1 cache provides an

8-KByte instruction cache and an 8-KByte data cache, both closely coupled to the pipeline. The

second-level cache provides 256-KByte, 512-KByte, or 1-MByte static RAM that is coupled to

the core processor through a full clock-speed 64-bit cache bus.

2-7

INTRODUCTION TO THE IA-32 INTEL ARCHITECTURE

The centerpiece of the P6 processor micro-architecture is an out-of-order execution mechanism

called dynamic execution. Dynamic execution incorporates three data-processing concepts:

•

•

Deep branch prediction allows the processor to decode instructions beyond branches to

keep the instruction pipeline full. The P6 processor family implements highly optimized

branch prediction algorithm to predict the direction of the instruction.

Dynamic data flow analysis requires real-time analysis of the flow of data through the

processor to determine dependencies and to detect opportunities for out-of-order

instruction execution. The out-of-order execution core can monitor many instructions and

execute these instructions in the order that best optimizes the use of the processor’s

multiple execution units, while maintaining the data integrity.

Speculative execution refers to the processor’s ability to execute instructions that lie

beyond a conditional branch that has not yet been resolved, and ultimately to commit the

results in the order of the original instruction stream. To make speculative execution

possible, the P6 processor micro-architecture decouples the dispatch and execution of

instructions from the commitment of results. The processor’s out-of-order execution core

uses data-flow analysis to execute all available instructions in the instruction pool and

store the results in temporary registers. The retirement unit then linearly searches the

instruction pool for completed instructions that no longer have data dependencies with

other instructions or unresolved branch predictions. When completed instructions are

found, the retirement unit commits the results of these instructions to memory and/or the

IA-32 registers (the processor’s eight general-purpose registers and eight x87 FPU data

registers) in the order they were originally issued and retires the instructions from the

instruction pool.

•

2.2.2.

Streaming SIMD Extensions 2 (SSE2) Technology

The Intel Pentium 4 processor introduced the SSE2 extensions. SSE2 extensions offer enhance-

ments to the Intel MMX technology and SSE extensions. The enhancements include operations

on new packed data formats and increased SIMD computational performance using 128-bit

registers for integer SIMD operation. A packed double-precision floating-point data type was

introduced along with several packed 128-bit integer data types. These data types allow packed

double-precision and single-precision floating-point and packed integer computations to be

performed in the XMM registers.

SIMD instructions include floating-point SIMD instructions, integer SIMD instructions,

instructions for conversion between SIMD floating-point data and SIMD integer data, and

instructions for conversion of packed data between XMM registers and MMX registers. The

floating-point SIMD instructions allow computations to be performed on packed double-preci-

sion floating-point values (two double-precision values per XMM register). The computation of

SIMD floating-point instructions, the single-precision and the double-precision floating-point

formats are compatible with IEEE Standard 754 for Binary Floating-Point Arithmetic. New

integer SIMD instructions provide flexible and higher dynamic range computational power by

supporting arithmetic operations on packed doubleword and quadword data as well as other

operations on packed byte, word, doubleword, quadword and double quadword data.

2-8

INTRODUCTION TO THE IA-32 INTEL ARCHITECTURE

In addition to new 128-bit SIMD instructions, there are 128-bit enhancements to 68 integer

SIMD instructions. These operated solely on 64-bit MMX registers in the Pentium II and

Pentium III processors. Those 64-bit integer SIMD instructions were enhanced to support oper-

ation on 128-bit XMM registers in the Pentium 4 processor. These enhanced integer SIMD

instructions allow software developers to have maximum flexibility by writing SIMD code with

either XMM registers or MMX registers.

The Intel Pentium 4 processor’s features enable software developers to deliver new levels of

performance in multimedia applications ranging from 3-D graphics, video

decoding/encoding, to speech recognition. The processor’s packed double-precision floating-

point instructions enhance performance for applications that require greater range and preci-

sion, including scientific and engineering applications and advanced 3-D geometry tech-

niques, such as ray tracing.

To speed up processing and improve cache usage, the SSE2 extensions offer several new

instructions that allow application programmers to control the cacheability of data. These

instructions provide the ability to stream data in and out of the registers without disrupting the

caches and the ability to prefetch data before it is actually used.

The new architectural features introduced with the SSE2 extensions do not require new oper-

ating system support. This is because the SSE2 extensions do not introduce new architectural

states, and the FXSAVE/FXRSTOR instructions, which supports the SSE extensions, also

supports SSE2 extensions and are sufficient for saving and restoring the state of the XMM regis-

ters, the MMX registers, and the x87 FPU registers during a context switch. The CPUID instruc-

tion has been enhanced to allow operating system or applications to identify for the existence of

the SSE and SSE2 features.

The SSE2 extensions are accessible in all IA-32 architecture operating modes on the Intel

Pentium 4 and Intel Xeon processors. Both processors maintain IA-32 software compatibility

meaning all existing software continues to run correctly, without modification on the Pentium 4,

Intel Xeon, and future IA-32 processors that incorporate the SSE2 extensions. Also, existing

software continues to run correctly in the presence of applications that make use of the SSE2

instructions.

2.2.3.

The Intel® NetBurst™ Micro-Architecture

The Intel NetBurst micro-architecture provides:

•

The Rapid Execution Engine

— Arithmetic Logic Units (ALUs) run at twice the processor frequency

— Basic integer operations executes in 1/2 processor clock tick

— Provides higher throughput and reduced latency of execution

•

Hyper-Pipelined Technology

— Twenty-stage pipeline to enable industry-leading clock rates for desktop PCs and

servers

2-9

INTRODUCTION TO THE IA-32 INTEL ARCHITECTURE

— Frequency headroom and scalability to continue leadership into the future

•

Advanced Dynamic Execution

— Deep, out-of-order, speculative execution engine.

•

•

•

•

•

Up to 126 instructions in flight

Up to 48 loads and 24 stores in pipeline

Reduces the misprediction penalty associated with deeper pipelines

Advanced branch prediction algorithm

4K-entry branch target array

— Enhanced branch prediction capability

•

New cache subsystem

— First level caches

•

•

•

•

•

•

Advanced Execution Trace Cache stores decoded instructions

Execution Trace Cache removes decoder latency from main execution loops

Execution Trace Cache integrates path of program execution flow into a single

line

Low latency data cache with 2 cycle latency

Full-speed, unified 8-way Level 2 on-die Advance Transfer Cache

Bandwidth and performance increases with processor frequency

— Second level cache

•

High-performance, quad-pumped bus interface to the Intel NetBurst micro-architecture

system bus

— Supports quad-pumped, scalable bus clock to achieve 4X effective speed

— Capable of delivering up to 3.2 GB of bandwidth per second (Pentium 4 and Intel

Xeon processors)

•

•

•

Superscalar issue to enable parallelism

Expanded hardware registers with renaming to avoid register name space limitations

128-byte cache line size (two 64-byte sectors)

Figure 2-2 is an overview of the Intel NetBurst micro-architecture. This micro-architecture pipe-

line is made up of three sections: (1) the front end pipeline (2) the out-of-order execution core,

and (3) the retirement unit.

2-10

INTRODUCTION TO THE IA-32 INTEL ARCHITECTURE

System Bus

Frequently used paths

Less frequently used paths

Bus Unit

3rd Level Cache

Optional, Server Product Only

2nd Level Cache

8-Way

1st Level Cache

4-way

Front End

Trace Cache

Microcode ROM

Fetch/Decode

Execution

Out-Of-Order Core

Retirement

BTBs/Branch Prediction

Branch History Update

Figure 2-2. The Intel NetBurst Micro-Architecture

2.2.3.1.

THE FRONT END PIPELINE

The front end supplies instructions in program order to the out-of-order execution core. It

performs a number of functions:

•

•

•

•

•

•

•

•

Prefetches IA-32 instructions that are likely to be executed

Fetches instructions that have not already been prefetched

Decodes IA-32 instructions into micro-operations

Generates microcode for complex instructions and special-purpose code

Delivers decoded instructions from the execution trace cache

Predicts branches using highly advanced algorithm

The pipeline is designed to address common problems in high-speed, pipelined microproces-

sors. Two of these problems contribute to major sources of delays:

Time to decode instructions fetched from the target

Wasted decode bandwidth due to branches or branch target in the middle of cache lines

The operation of the pipeline’s trace cache addresses these issues. Instructions are constantly

being fetched and decoded by the translation engine (part of the fetch/decode logic) and built

2-11

INTRODUCTION TO THE IA-32 INTEL ARCHITECTURE

into sequences of µops called traces. At any time, multiple traces (representing prefetched

branches) are being stored in the trace cache. The trace cache is searched for the instruction that

follows the active branch. If the instruction also appears as the first instruction in a pre-fetched

branch, the fetch and decode of instructions from the memory hierarchy ceases and the pre-

fetched branch becomes the new source of instructions (see Figure 2-2).

The trace cache and the translation engine have cooperating branch prediction hardware. Branch

targets are predicted based on their linear addresses using branch target buffers (BTBs) and

fetched as soon as possible.

2.2.3.2.

OUT-OF-ORDER EXECUTION CORE

The out-of-order execution core’s ability to execute instructions out of order is a key factor in

enabling parallelism. This feature enables the processor to reorder instructions so that if one µop

is delayed, other µops may proceed around it. The processor employs several buffers to smooth

the flow of µops.

The core is designed to facilitate parallel execution. It can dispatch up to six µops per cycle (this

exceeds trace cache and retirement µop bandwidth). Most pipelines can start executing a new

µop every cycle, so several instructions can be in flight at a time for each pipeline. A number of

arithmetic logical unit (ALU) instructions can start at two per cycle; many floating-point instruc-

tions can start once every two cycles.

Note that µops can begin execution, out of order, as soon as their data inputs are ready and

resources are available.

2.2.3.3.

RETIREMENT UNIT

The retirement unit receives the results of the executed µops from the out-of-order execution

core and processes the results so that the architectural state updates according to the original

program order. Instructions retire in program order. IA-32 exceptions always occur in program

order. This means that exceptions do not occur speculatively; they must occur in correct order

so that there can be an appropriate restart after an exception.

When a µop completes and writes its result, it is retired. Up to three µops may be retired per

cycle. The Reorder Buffer (ROB) is the unit in the processor which buffers completed µops,

updates the architectural state in order, and manages the ordering of exceptions. The retirement

section also keeps track of branches and sends updated branch target information to the BTB.

The BTB then purges pre-fetched traces that are no longer needed.

2.2.4.

Hyper-Threading Technology

Hyper-Threading (HT) Technology was developed to improve the performance of IA-32 proces-

sors when executing multi-threaded operating system and application code or single-threaded

applications under multi-tasking environments. The technology enables a single physical

processor to execute two or more separate code streams (threads) concurrently.

2-12

INTRODUCTION TO THE IA-32 INTEL ARCHITECTURE

Architecturally, an IA-32 processor that supports HT Technology consists of two or more logical

processors, each of which has its own IA-32 architectural state. Each logical processor consists

of the IA-32 data registers, segment registers, control registers, debug registers and most of the

MSRs. Each also has its own advanced programmable interrupt controller (APIC).

Figure 2-3 shows a comparison of an IA-32 processor with HT Technology (implemented with

two logical processors) and a traditional dual processor system.

IA-32 Processor with

Hyper-Threading Technology

AS

AS

Traditional Multiple Processor (MP) System

AS

AS

Processor Core

Processor Core

Processor Core

IA-32 processor

Two logical processors

that share a single core

IA-32 processor

IA-32 processor

Each processor is a

separate physical

package

AS = IA-32 Architectural State

Figure 2-3. Comparison of an IA-32 Processor with Hyper-Threading Technology and a

Traditional Dual Processor System

Unlike a traditional MP system configuration that uses two or more separate physical IA-32

processors, the logical processors in an IA-32 processor with HT Technology share the core

resources of the physical processor. This includes the execution engine and the system bus inter-

face. After power up and initialization, each logical processor can be independently directed to

execute a specified thread, interrupted, or halted.

HT Technology leverages the process and thread-level parallelism found in contemporary oper-

ating systems and high-performance applications by providing two or more logical processors

on a single chip. This configuration allows two or more threads3 to be executed simultaneously

on each a physical processor. Each logical processor executes instructions from an application

thread using the resources in the processor core. The core executes these threads concurrently,

3. In the remainder of this document, the term “thread” will be used as a general term for the terms “pro-

cess” and “thread.”

2-13

INTRODUCTION TO THE IA-32 INTEL ARCHITECTURE

using out-of-order instruction scheduling to maximize the use of execution units during each

clock cycle.

2.2.4.1.

NOTES ON IMPLEMENTATION

Hyper-Threading (HT) Technology was introduced into the IA-32 architecture in the Intel Xeon

processor MP and in later steppings of the Intel Xeon processor. It is also supported by the Intel

Pentium 4 processor at 3.06 GHz or higher. All HT Technology configurations require a chipset

and BIOS that utilize the technology, and an operating system that includes optimizations for

HT technology. See www.intel.com/info/hyperthreading for more information.

At the firmware (BIOS) level, the basic procedures to initialize the logical processors in a

processor supporting HT Technology are the same as those for a traditional DP or MP platform4.

The same mechanisms that are described in the Multiprocessor Specification Version 1.4 to

power-up and initialize physical processors in an MP system apply to the logical processors in

a HT Technology-enabled processor. An operating system designed to run on a traditional DP

or MP platform uses the CPUID instruction to detect the presence of an IA-32 processor with

Hyper-Threading Technology and the number of logical processors it provides.

Although existing operating system and application code should run correctly on a processor

that supports HT Technology, some code modifications are recommended to get the optimum

benefit. These modifications are discussed in the IA-32 Intel Architecture Software Developer’s

Manual, Volume 3, in the section titled “Required Operating System Support” in Chapter 7,

Multiple Processor Management.

2.3.

MOORE’S LAW AND IA-32 PROCESSOR GENERATIONS

In the mid-1960s, Intel cofounder and Chairman Emeritus Gordon Moore had this observation:

“the number of transistors that would be incorporated on a silicon die would double every 18

months for the next several years.” Over the past three and half decades, this prediction known

as “Moore's Law has continued to hold true.

The computing power and the complexity (or roughly, the number of transistors per processor)

of Intel architecture processors has grown in close relation to Moore's law. By taking advantage

of new process technology and new micro-architecture designs, each new generation of IA-32

processors has demonstrated frequency-scaling headroom and new performance levels over the

previous generation processors.

The key features of the Intel Pentium 4 processor, Intel Xeon processor, Intel Xeon processor

MP, Pentium III and Pentium III Xeon processors with advanced transfer cache are shown in

Table 2-1. Older generation IA-32 processors, which do not employ on-die Level 2 cache, are

shown in Table 2-2.

4. Some relatively simple enhancements to the MP initialization algorithm are needed.

2-14

INTRODUCTION TO THE IA-32 INTEL ARCHITECTURE

Table 2-1. Key Features of Most Recent IA-32 Processors

Date

Intro-

duced

2000

Clock

Frequency Transis-

Micro-at Intro-tors Per

ArchitectureductionDie

Intel NetBurst

Micro-

architecture

1.50 GHz

42 M

System Max.

Bus Extern.

Band- Addr.

width Space

3.2

GB/s

Intel

Processor

Pentium 4

Processor

Register

Sizes1

GP: 32

FPU: 80

MMX: 64

XMM: 128

On-Die

Caches2

64 GB 12K µop

Execution

Trace

Cache;

8KB L1;

256-KB L2

64 GB 12K µop

Trace

Cache;

8-KB L1;

256-KB L2

64 GB 12K µop

Trace

Cache;

8-KB L1;

512-KB L2

64 GB 12K µop

Trace

Cache;

8-KB L1;

256-KB L2;

1-MB L3

64 GB 12K µop

Execution

Trace

Cache;

8KB L1;

512-KB L2

64 GB L1: 64KB

L2: 1MB

Intel Xeon

Processor

2001

Intel NetBurst

Micro-

architecture

1.70 GHz

42 M

GP: 32

FPU: 80

MMX: 64

XMM: 128

GP: 32

FPU: 80

MMX: 64

XMM: 128

3.2

GB/s

Intel Xeon

Processor

2002

Intel NetBurst

Micro-

architecture;

Hyper-

Threading

Technology

Intel NetBurst

Micro-

architecture;

Hyper-

Threading

Technology

Intel NetBurst

Micro-

architecture;

Hyper-

Threading

Technology

Intel Pentium

M Processor

2.20 GHz

55 M

3.2

GB/s

Intel Xeon

Processor

MP

2002

1.60 GHz

108 M

GP: 32

FPU: 80

MMX: 64

XMM: 128

3.2

GB/s

Intel

Pentium 4

Processor

supporting

Hyper-

Threading

Technology

Intel

Pentium M

Processor

NOTES

2002

3.06 GHz

55M

GP: 32

FPU: 80

MMX: 64

XMM: 128

4.2

GB/s

2003

1.60 GHz

77M

GP: 32

FPU: 80

MMX: 64

XMM: 128

3.2

GB/s

1. The register size and external data bus size are given in bits.

2. First level cache is denoted using the abbreviation L1, 2nd level cache is denoted as L2. The size of L1

includes the first-level data cache and the instruction cache where applicable, but does not include the

trace cache.

2-15

INTRODUCTION TO THE IA-32 INTEL ARCHITECTURE

Table 2-2. Key Features of Previous Generations of IA-32 Processors

Date

Intro-

duced

1978

1982

1985

1989

1993

1995

Max. Clock

Frequency

at Intro-

duction

8 MHz

12.5 MHz

20 MHz

25 MHz

60 MHz

200 MHz

Transis

-tors

per Die

29 K

134 K

275 K

1.2 M

3.1 M

5.5 M

Ext.

Data

Bus

Size2

16

16

32

32

64

64

Max.

Extern.

Addr.

Space

1 MB

16 MB

4 GB

4 GB

4 GB

64 GB

Intel Processor

8086

Intel 286

Intel386 DX Processor

Intel486 DX Processor

Pentium Processor

Pentium Pro Processor

Register

Sizes1

16 GP

16 GP

32 GP

32 GP

80 FPU

32 GP

80 FPU

32 GP

80 FPU

32 GP

80 FPU

64 MMX

32 GP

80 FPU

64 MMX

128

XMM

32 GP

80 FPU

64 MMX

128

XMM

Caches

None

Note 3

Note 3

L1: 8KB

L1:16KB

L1: 16KB

L2: 256KB

or 512KB

L1: 32KB

L2: 256KB

or 512KB

L1: 32KB

L2: 512KB

Pentium II Processor

1997

266 MHz

7M

64

64 GB

Pentium III Processor

1999

500 MHz

8.2 M

64

64 GB

Pentium III and

Pentium III Xeon

Processors

1999

700 MHz

28 M

64

64 GB

L1: 32KB

L2: 256KB