# The Power of Water

When watching a river roll by, it's hard to imagine the force it's carrying. If you have ever been white-water rafting, then you've felt a small part of the river's power. White-water rapids are created as a river, carrying a large amount of water downhill, bottlenecks through a narrow passageway. As the river is forced through this opening, its flow quickens. Floods are another example of how much force a tremendous volume of water can have.

Hydropower plants harness water's energy and use simple mechanics to convert that energy into electricity. Hydropower plants are actually based on a rather simple concept -- water flowing through a dam turns a turbine, which turns a generator.

Here are the basic components of a conventional hydropower plant:

Dam - Most hydropower plants rely on a dam that holds back water, creating a large reservoir. Often, this reservoir is used as a recreational lake

Intake - Gates on the dam open and gravity pulls the water through the penstock, a pipeline that leads to the turbine. Water builds up pressure as it flows through this pipe.

Turbine - The water strikes and turns the large blades of a turbine, which is attached to a generator above it by way of a shaft. The most common type of turbine for hydropower plants is the Francis Turbine, which looks like a big disc with curved blades. A turbine can weigh as much as 172 tons and turn at a rate of 90 revolutions per minute (rpm), according to the Foundation for Water & Energy Education (FWEE).

Generators - As the turbine blades turn, so do a series of magnets inside the generator. Giant magnets rotate past copper coils, producing alternating current (AC) by moving electrons.

Transformer - The transformer inside the powerhouse takes the AC and converts it to higher-voltage current.

Power lines - Out of every power plant come four wires: the three phases of power being produced simultaneously plus a neutral or ground common to all three.

Outflow – Used water is carried through pipelines, called tailraces, and re-enters the river downstream.

Photo courtesy U.S. Bureau of Reclamation The shaft that connects the turbine and generator

The water in the reservoir is considered stored energy. When the gates open, the water flowing through the penstock becomes kinetic energy because it's in motion. The amount of electricity that is generated is determined by several factors. Two of those factors are the volume of water flow and the amount of hydraulic head. The head refers to the distance between the water surface and the turbines. As the head and flow increase, so does the electricity generated. The head is usually dependent upon the amount of water in the reservoir.

# Pumped-Storage Plants

There's another type of hydropower plant, called the pumped-storage plant. In a conventional hydropower plant, the water from the reservoir flows through the plant, exits and is carried down stream. A pumped-storage plant has two reservoirs:

- Upper reservoir - Like a conventional hydropower plant, a dam creates a reservoir. The water in this reservoir flows through the hydropower plant to create electricity.

- Lower reservoir - Water exiting the hydropower plant flows into a lower reservoir rather than re-entering the river and flowing downstream.

Using a reversible turbine, the plant can pump water back to the upper reservoir. This is done in off-peak hours. Essentially, the second reservoir refills the upper reservoir. By pumping water back to the upper reservoir, the plant has more water to generate electricity during periods of peak consumption.

The Generator
The heart of the hydroelectric power plant is the generator. Most hydropower plants have several of these generators.

Photo courtesy U.S. Bureau of Reclamation The giant generators at Hoover Dam produce more than 2,000 megawatts.

The generator, as you might have guessed, generates the electricity. The basic process of generating electricity in this manner is to rotate a series of magnets inside coils of wire. This process moves electrons, which produces electrical current.

Inside a hydropower plant generator

The Hoover Dam has a total of 17 generators, each of which can generate up to 133 megawatts. The total capacity of the Hoover Dam hydropower plant is 2,074 megawatts. Each generator is made of certain basic parts:

- Shaft

- Excitor

- Rotor

- Stator

As the turbine turns, the excitor sends an electrical current to the rotor. The rotor is a series of large electromagnets that spins inside a tightly-wound coil of copper wire, called the stator. The magnetic field between the coil and the magnets creates an electric current.

# Hydrologic Cycle

Hydropower plants take advantage of a naturally occurring, continuous process -- the process that causes rain to fall and rivers to rise. Every day, our planet loses a small amount of water through the atmosphere as ultraviolet rays break water molecules apart. But at the same time, new water is emitted from the inner part of the Earth through volcanic activity. The amount of water created and the amount of water lost is about the same.

At any one time, the world's total volume of water is in many different forms. It can be liquid, as in oceans, rivers and rain; solid, as in glaciers; or gaseous, as in the invisible water vapor in the air. Water changes states as it is moved around the planet by wind currents. Wind currents are generated by the heating activity of the sun. Air-current cycles are created by the sun shining more on the equator than on other areas of the planet.

Air-current cycles drive the Earth's water supply through a cycle of its own, called the hydrologic cycle. As the sun heats liquid water, the water evaporates into vapor in the air. The sun heats the air, causing the air to rise in the atmosphere. The air is colder higher up, so as the water vapor rises, it cools, condensing into droplets. When enough droplets accumulate in one area, the droplets may become heavy enough to fall back to Earth as precipitation.

The hydrologic cycle

The hydrologic cycle is important to hydropower plants because they depend on water flow. If there is a lack of rain near the plant, water won't collect upstream. With no water collecting up stream, less water flows through the hydropower plant and less electricity is generated.